Development Project ESP32C3-Pro Watering System

Suggestion from Claude:

This is a well-defined project! Based on your requirements the architecture is clear:
No WiFi available → BLE is the perfect choice.

### System Architecture
iOS App (BLE Central)
    ↕ BLE
ESP32-C3 (BLE Peripheral)
    ├── Valve 1 (GPIO) → Water zone 1
    ├── Valve 2 (GPIO) → Water zone 2
    ├── Rain sensor (GPIO input)
    ├── OLED display (I2C) → Status display
    └── RTC module (I2C) → Keeps time without WiFi

### Key design decisions to make
1 — Real Time Clock (RTC) Since there is no WiFi, the ESP32 cannot sync time via NTP. You need an external RTC module to keep accurate time even when powered off. The most common and reliable one is the DS3231 — very accurate, cheap, available on Taobao, connects via I2C (same bus as your OLED).
2 — Valve control Valves typically run on 12V or 24V AC/DC solenoids. The ESP32 GPIO (3.3V, 40mA max) cannot drive them directly. You need a relay module or MOSFET driver board between the GPIO and the valve. A standard 4-channel relay module works perfectly and is very cheap.
3 — Rain sensor A simple digital rain sensor module outputs HIGH/LOW depending on rain detected. Connects directly to a GPIO input pin. Some also have an analog output for rain intensity.
4 — Power Mounted outside with no WiFi infrastructure suggests it may also be battery powered or has a dedicated power supply. Worth planning upfront.

### Suggested hardware list
Component	Purpose	Interface
ESP32-C3	Main controller	—
DS3231 RTC module	Keep time without WiFi	I2C
SSD1312 OLED	Status display	I2C
Rain sensor module	Detect rain	GPIO digital in
4-channel relay module	Drive valves	GPIO digital out
Solenoid valves	Control water flow	Via relay
12V or 24V power supply	Power valves + ESP32	—

### Software architecture
The firmware has four main components:
┌─────────────────────────────────────┐
│ ESP32-C3 Firmware │
├─────────────────────────────────────┤
│ Scheduler │ checks RTC time │
│ │ triggers valve open │
│ │ respects rain sensor │
├─────────────────────────────────────┤
│ Valve ctrl │ open/close valves │
│ │ enforce max open time│
├─────────────────────────────────────┤
│ BLE server │ receive schedule │
│ │ from iOS app │
│ │ send status to app │
├─────────────────────────────────────┤
│ Display │ show time, next │
│ │ watering, rain status│
└─────────────────────────────────────┘

### BLE data exchange with iOS
The ESP32 exposes BLE characteristics — think of them as variables the iOS app can read and write:
Characteristic	Direction	Content
SCHEDULE	iOS → ESP32	Watering times + duration
STATUS	ESP32 → iOS	Current time, next watering, rain, valve state
RAIN	ESP32 → iOS	Rain sensor reading
MANUAL	iOS → ESP32	Force open/close a valve

### Suggested project phases
Phase 1 — Hardware foundation
- DS3231 RTC reading/writing time
- Relay module opening/closing valves
- Rain sensor reading
- All status on OLED display
Phase 2 — Scheduler
- Store watering schedule in ESP32 flash memory (LittleFS)
- Check RTC time every minute
- Open valve at scheduled time, close after defined duration
- Skip if rain sensor active
Phase 3 — BLE
- ESP32 advertises as BLE peripheral
- iOS app connects and reads/writes schedule
- iOS app shows live status
Phase 4 — iOS app
- Simple Swift app with CoreBluetooth
- Set schedule (days, times, duration per zone)
- View current status and rain condition
- Manual valve control for testing

### Safety features to build in
These are important for a watering system:
- Maximum valve open time — even if software crashes, never keep a valve open longer than e.g. 30 minutes. Implement a hardware-independent timer that force-closes.
- Rain inhibit — if rain sensor active, skip scheduled watering and log it.
- Manual override — iOS app can force open/close any valve for testing.
- Status persistence — save last known schedule to flash so it survives power cuts.

### Suggested next steps
I suggest we build this phase by phase. The logical first step is:
1. Get the DS3231 RTC working — reading and setting time via I2C
2. Display the current time on your OLED
3. Then add valve control via relay
4. Then the scheduler
5. Then BLE
Do you already have the DS3231 and relay module, or are you still sourcing components? And how many watering zones (valves) do you need?